## Slide 1: Screening a system—laboratory approaches to assessing features of a bioremediation system
3/23/23

## Slide 2: Module Outline
Intro
Review
Apply
Test
Design
M2D6: Applying remediation strategies—advantages and pitfalls
M2D7: Engineering a problem-specific bioremediation solution
M2D8: Comm Lab
M2D4: Screening a system—assessing features of a bioremediation system
M2D5: Analysis of elemental metals – laboratory and field approaches
M2D1: Environmental heavy metal contamination
M2D2: Model system – target selection and engineering approach
M2D3: Model system – choosing a chassis host

## Slide 3: Lecture overview
Is our mutant protein expressed?
Does our mutant transporter show any differential ability to take up metal?
Does our cell tolerate metal exposure and uptake?
3 key parameters of our bioremediation system should be established

## Slide 4: Protein expression

## Slide 5: Fet4 mutant expression can be established with immunofluorescence
Antibodies against protein or incorporated tag
Confirms that mutant protein is translated and trafficked as expected
Automated 96 well microscopy for adherent cells

## Slide 6: Flow cytometry can also be used to quantify protein expression
Rego. 2021. Addgene
side scatter
forward
scatter
Cells expressing mutant protein are labeled with fluorescent antibodies
Labeled cells are passed in single file in front of a laser and visible light source
  the scatter of the visible light provides information about cell size and granularity
  fluorescent signal indicates protein labeling by antibody

## Slide 7: Metal uptake

## Slide 8: ICP-OES/MS can measure elemental concentration in a sample
Metal concentration can be directly quantified
Inductively Coupled Plasma Optical Emission Spectroscopy (ICP-OES)

## Slide 9: Electron microscopy can visualize metal collection in a cell
Transmission Electron Microscopy (TEM)
  send electron beam through a sample
  generated image is shaded according to density
TEM micrograph of root section from plant exposed to Cd for 14 days
  Identified granules containing Cd in the cell wall of pericycle cells
2000x magnification
20,000x magnification
Wojcik, 2004
Notes: TEM= transmission electron microscopy– better for internal composition of materials, where SEM (Scanning electron microscopy) shows us more about morphology

## Slide 10: Radioactive metal isotopes can be utilized to monitor metal presence
Incubate cells with radioactive isotope of metal
  Rapid wash to remove any radioactive material not bound to or accumulated within the cell
  Use gamma scintillation counter to convert radioactive decay to light to an electrical pulse
  High sensitivity
Stanford Scintillation Materials Group
Gaither, 2001
Brandel Cell Harvester

## Slide 11: Engineered sensors can be used to detect metal in a cell
Förster Resonance Energy Transfer (FRET)
  Laser excited donor fluorophore
  Acceptor fluorophore emits fluorescent signal
Bioluminescence Resonance Energy Transfer (BRET)
  Bioluminescent luciferase excites the acceptor flurophore
Fluorescent probes
  small enough to cross a membrane and bind to intracellular metal
  not as sensitive as the sensors
Aper. 2016

## Slide 12: Cell tolerance of metal accumulation

## Slide 13: Different metrics can be used to assess cell viability
Growth rate
Membrane integrity
Metabolic activity

## Slide 14: Spotting assay can be used to count colonies and compare growth under different conditions
Commonly used to evaluate bacterial or yeast growth and survival
Measure the density of cells within a single spot of defined size
  Count colonies
  Densitometry
Identify common dilution that will allow for most accurate comparison across groups
Petropavlovskiy. 2020

## Slide 15: Vital dyes can be used to establish membrane integrity of cells
Colormetric dyes
Neutral red
  weak cation dye
  passes across intact plasma membranes to concentrate in organelles like vacuoles and lysosomes
  damage to those membranes prevents the incorporation of the dye
  Red= alive
Evans blue
  anionic dye
  impermeable to membrane of living cells but able to accumulate in cells with compromised plasma membrane
  Blue = dead
  trypan blue is another example
Evans blue dye
Neutral red

## Slide 16: Nuclear fluorescent dyes can be used to indicate loss of membrane integrity
SYTOX Green is a probe that cannot cross intact membranes
One inside the nucleus, it binds to nucleic acids and fluoresces

## Slide 17: LIVE/DEAD assays can simultaneously mark both states of cells within a population
SYTO 9 green-fluorescent nucleic acid stain
  Can cross intact membranes and label all cells in a population
Propidium iodide red-fluorescent nucleic acid stain
  Only enters cells with damaged membranes
  Causes a reduction in the SYTO 9 stain fluorescence via FRET
Cells with intact membranes stain fluorescent green
Cells with damaged membranes stain fluorescent red

## Slide 18: Reduction of tetrazolium salts creates color change proportional to metabolic activity
Tetrazolium salts can reduced into formazan as a by product of metabolic processes such as oxidative phosphorylation
  Color change is proportional to metabolic activity
MTT = purple formazan precipitates
  production kills cells
  less sensitive
  less expensive
WST-8 = soluble orange formazan
  cells survive assay
  more sensitive
  more expensive
Held. 2009

## Slide 19: ATP content can be used as a proxy for cellular physiology and metabolic activity
Luciferase utilizes ATP to oxidize Luciferin to Oxyluciferin
  Emits light as a result
Luminescence is proportional to ATP and thus to cell metabolic activity
Metabolic activity can change without resulting in cell death
  In contrast to loss of membrane integrity
Promega

## Slide 20: What are you doing in lab today?
Experimental lull!
  Biology moves slower than grand plans…
Align sequencing to determine presence of mutations
Prepare coverslips for the immunofluorescence experiment that begins after Spring break/ Journal article presentation week