## Slide 1
L3 – Small Molecule Microarrays
February 15, 2018
Notes: Today we will talk about the method we are using to search for small molecules to bind to FKBP12. This is a method that is near and dear to my heart because it goes all the way back to 1998, probably when most of you were still in diapers.

## Slide 2
The view from 2000

## Slide 3
~ 15 years on from the Human Genome Project

## Slide 4
~ 15 years on from the Human Genome Project

## Slide 5
~ 15 years on from the Human Genome Project

## Slide 6
Chemical probes of disease biology
patient samples reveal
list of disease genes
discover or develop small
molecules that reverse the
impact of disease genes
physiologic settings to test
the impact of disease genes
Approach: use small molecules to test emerging concepts in human disease
in physiologically relevant settings
Output: validated small-molecule probe to facilitate human clinical development
or diagnostic applications
Notes: Why does someone like me care so much about small molecules? Probes of biology!
Unlike other types of probes dose control, temporal control, spatial control, MANY PROTEINS HAVE MORE THAN ONE FUNCTION, Modulate individual functions
Finally, small molecules can serve as leads for drug development or lower the activation barrier for the development of other drugs against a target.

## Slide 7
‘Undruggable’ targets are aplenty
disordered proteins
e.g. amyloids, transcription factors, enzymes
DNA binding proteins
protein-protein interactors
e.g. transcription factors,
extracellular growth factors,
scaffold proteins
integral membrane proteins
e.g. cell adhesion proteins,
enzymes, receptors

## Slide 8
1998 – ‘on-bead’ binding assays
fluorescent
bead
no binding
assay positive
Library = 2.18M on
90 µm Tentagel beads
rhodamine dye
540/625 nm
’Gradbot’
Angela

## Slide 9
1998 - other binding assay formats
Ligand
Protein
KDeq, DG, DH
isothermal titration calorimetry
measure changes in temperature
upon binding
fluorescence polarization
measure changes in rate of rotation
upon binding
Notes: ITC is a quantitative technique that can determine the binding affinity (Ka), enthalpy changes (ΔH), and binding stoichiometry (n) of the interaction between two or more molecules in solution. From these initial measurements, Gibbs energy changes (ΔG) and entropy changes (ΔS) can be determined using the relationship:
ΔG = -RTlnKa = ΔH-TΔS where R is the gas constant and T is the absolute temperature).
ITC is one of the latest techniques to be used in characterizing binding affinity of ligands for proteins. It is typically used as a secondary screening technique in high throughput screening. ITC is particularly useful as it gives not only the binding affinity, but also the thermodynamics of the binding. This thermodynamic characterization allows for further optimization of compounds.[4]
Observations are plotted as the power needed to maintain the reference and the sample cell at an identical temperature against time. As a result, the experimental raw data consists of a series of spikes of heat flow (power), with every spike corresponding to one ligand injection. These heat flow spikes/pulses are integrated with respect to time, giving the total heat exchanged per injection. The pattern of these heat effects as a function of the molar ratio [ligand]/[macromolecule] can then be analysed to give the thermodynamic parameters of the interaction under study. It should be noted that degassing samples is often necessary in order to obtain good measurements as the presence of gas bubbles within the sample cell will lead to abnormal data plots in the recorded results. The entire experiment takes place under computer control.

## Slide 10
Pat Brown, Stanford
follow changes in gene expression during yeast sporulation
Late 1990s - ‘Spatially addressable systems’
Notes: Briefly, thousands of discrete DNA sequences (e.g. all of the 6,200 known and predicted genes in s. cerevisiae) are robotically printed onto a glass microscope slide using an arrayer (X-Y-Z robot). To compare the relative abundance of genes in two samples (for example the total mRNA populations isolated from 2 cell populations) two smaples are labeled with different fluorescent dyes (e.g. a red and gree dye). The samples are mixed and applied to the array (called hybridization) and fluorescence measurements are made to determine a ratio of red to green.
This was one of a couple of array-based methods that were being developed in the mid-90s, mostly in companies, but the simplicity of this design took hold in academia. TheStanford team went so far as to publish all of the methods for making the robot on the Brown lab website.
One week after running my bead screen, we started constuction of a clean room to make the robot.

## Slide 11
Small Molecule Microarrays (SMMs)
compound stock solutions
SMM manufacture and screening
screened SMM

## Slide 12
Proof-of-concept experiments for SMMs
detecting known protein-ligand interactions
J. Am. Chem. Soc. 121, 7967-7968, 1999
Streptavidin
Anti-Digoxin mAb
FKBP12

## Slide 13
Proof-of-concept experiments for SMMs
evaluating affinities and multiplexed formats
J. Am. Chem. Soc. 121, 7967-7968, 1999
KD (nM): 2,600 140 8.8

## Slide 14
Capture chemistries for making SMMs
Photoaffinity
capture
Kanoh et al., Angew. Chem. Int. Ed. 42, 5584-5597, 2003
Diels-Alder
benzoquinone
SAM
Houseman, B.T., Mrksich, M. Chem. Biol. 9, 443-454, 2002
Köhn et al., Angew. Chem. Int. Ed. 42, 5830-5834, 2003
phosphine glass
Staudinger ligation
Hergenrother et al., J. Am. Chem. Soc. 122, 7849-7850, 1999
Barnes-Seeman et al., Angew. Chem. Int. Ed. 42, 2376-2379, 2003

## Slide 15
Photoaffinity
capture
Kanoh et al., Angew. Chem. Int. Ed. 42, 5584-5597, 2003
Diels-Alder
benzoquinone
SAM
Houseman, B.T., Mrksich, M. Chem. Biol. 9, 443-454, 2002
Köhn et al., Angew. Chem. Int. Ed. 42, 5830-5834, 2003
phosphine glass
Staudinger ligation
Hergenrother et al., J. Am. Chem. Soc. 122, 7849-7850, 1999
Barnes-Seeman et al., Angew. Chem. Int. Ed. 42, 2376-2379, 2003
Capture chemistries for making SMMs

## Slide 16
Capture chemistries for making SMMs
Bradner, J. E., McPherson, O. M., Mazitschek, R. M., Barnes-Seeman, D., Shen, J. P., Dhaliwal, J., Stevenson, K., Duffner, J. L., Park, S. B., Nghiem, P. T., Schreiber, S. L., Koehler, A. N., Chem Biol, 13, 493-504 (2006)
Bradner, J. E., McPherson, O. M., Koehler, A. N., Nature Protocols, 1, 2344-2352 (2006)

## Slide 17
SMMs contain compounds from a variety of sources
In silico analysis of 400,000 ‘National Library’ for screens:
>75% isocyanate-reactive

## Slide 18
Interactions with varying kinetics can be visualized
350 µm
rapamycin
AP1497
KD = 18 nM
Kd = 0.226 sec-1
KD = 0.5 nM
Kd = 0.000965 sec-1
42 min
2 min

## Slide 19
Detecting multiple interactions with Rapamycin
FRB
domain of mTOR
FKBP12
J Choi, J Chen, S L Schreiber, J Clardy, Science 1996, 273, 239-242.
FKBP12
FRB
KD = 0.5 nM
KD = 26 µM
300 µm
1 mM Rapamycin
0.2 mM Rapamycin

## Slide 20
SMMs containing natural product extracts
Schmitz, K., Haggarty, S.J., McPherson, O. M., Clardy, J., Koehler, A. N., J. Am. Chem. Soc., 129, 11346-11347, 2007
Didemnum roberti
misakinolide A
tubulin binder
manzamine A
eIF4a binder
stimulates IRES- and
cap-dependent translation
crude extracts
fractions of varying purity
SMM of extract fractions
1000 µm

## Slide 21
SMMs enable a new type of screen
target-directed assays in a native environment

## Slide 22
Binding screens involving cell lysates
Bradner, J. E., McPherson, O. M., Koehler, A. N., Nature Protocols, 1, 2344-2352 (2006)
control
transfection
(empty vector)
Flag-FKBP12
transfection
FKBP12
HEK-293T Cells
Tag
FKBP12
lyse cells
lyse cells

## Slide 23
Comparing detection methods using lysates
Detection via a Fluor-Labeled
Secondary Antibody
FKBP12
Flag
eGFP
FKBP12
Detection via Green
Fluorescent Protein
1 2 Captopril Glutathione
500 µm
Detection via anti-FKBP12 Antibody
and Labeled Secondary
FKBP12
Bradner, J.E., McPherson, O.M., Mazitschek, R., Barnes-Seeman, D., Shen, J.P., Dhaliwal, J., Stevenson, K., Duffner, J.L.,
Park, S.B., Nghiem, P., Schreiber, S.L., Koehler, A.N. Chem. Biol. 13, 493-504, 2006

## Slide 24
Binding screen using FKBP12 in cell lysates
Bradner, J.E., McPherson, O.M., Mazitschek, R., Barnes-Seeman, D., Shen, J.P., Dhaliwal, J., Stevenson, K., Duffner, J.L.,
Park, S.B., Nghiem, P., Schreiber, S.L., Koehler, A.N. Chem. Biol. 13, 493-504, 2006

## Slide 25
Analysis pipeline – the simple version

## Slide 26
A community effort

## Slide 27
A community effort

## Slide 28
Representative probes discovered by SMMs
KD = 0.6 µM (ITC)
inhibits pirin-Bcl3 interaction in cells
inhibits melanoma cell migration
Miyazaki et al, ACS Chem Biol 2010
Pirin from cell lysates
Discovery stories highlighted in - Vegas, A.J., Fuller, J. H., Koehler, A.N. Chem. Soc. Rev. 37, 1385-1394, 2008
KD = 3.1 µM (SPR)
analog of SMM hit that inhibits Shh signaling in cells and synthetic skin model
Stanton et al, Nature Chem Biol 2010
Sonic hedgehog
Aβ peptide
KD Aβ40mon ~ 9-17 µM (various methods) inhibits Aβ42-induced cytotoxicity in PC12 cells, accelerates fibril formation Chen et al, J. Am. Chem. Soc. 2010
HDAC inhibitor
BRD-2577
Ure2p
uretupamine
Hap3p
haptamide
Calmodulin
calmoduphilin
Calmodulin
calmodioxane
Calmodulin
NPC-15437
FKBP12
FKL-01
AURKA
1106.I16
Fyn
Bi-TAL
Fyn
TAL
Fyn
TAL-Cl

## Slide 29
Public access for SMM data sets

## Slide 30
ChemBank: an analytical tool for the community
assays (cell-based, biochemical, binding)
small molecules
relationship of structure to screen performance
relationships between assays (protein and phenotype)

## Slide 31
Spring 2017 FKBP12 screens
’Gradbot’
Rob

## Slide 32
Spring 2017 FKBP12 screens
each team screened
5,000 unique
compounds
16x16x48 = 12,288
2 replicate slides
4 replicates for each compound
’Gradbot’
Rob

## Slide 33
each team screened
5,000 unique
compounds
16x16x48 = 12,288
2 replicate slides
4 replicates for each compound
Spring 2017 FKBP12 screens

## Slide 34
Spring 2017 FKBP12 screen summary
Identify fluorescent spots on microarray images
Establish a threshold for statistical significance
Validate hits by eye
(76 compounds pass)

## Slide 35
Conserved substructures

## Slide 36
Our path to evaluate FKBP12 ligands
test ligands in FKBP12
binding assay
lab day 6
in silico cloning; overexpress FKBP12
lab days 1 & 2
purify and analyze FKBP12
lab days 3 and 4
+
complete data analysis
prioritize best ligands
lab day 7
test FKBP12 and ligands
in enzyme activity assay
lab day 5
IC50 = X µM
DT = Y °C
re-analyze screen data
lab day 2

## Slide 37
2/8/17 Lecture 1 Intro to chemical biology: small molecules, probes, and screens
2/13/17 Lecture 2 For the love of proteins: FKBP12 and immunophilins
2/15/17 Lecture 3 Small-molecule microarrays
2/21/17 No Lecture
2/22/17 Lecture 4 Quantitative evaluation of protein-ligand interactions
2/27/17 Lecture 5 A ligand discovery vignette: sonic hedgehog
3/1/17 Lecture 6 Engineering transcriptional responses with a small molecule
3/7/17 Lecture 7 Wrap up discussion: suggestions for how to report your findings
Our path to evaluate ligands - lectures